Circuit Documentation
Summary
This circuit is a complex system involving a Seeeduino XIAO microcontroller, two ULN2803 Darlington Arrays, multiple coin vibration motors, a BNO085 sensor, an MCP23S17 I/O expander, and a push button. The circuit is designed to control multiple vibration motors through the Darlington arrays, which are driven by the I/O expander. The Seeeduino XIAO serves as the main controller, interfacing with the I/O expander and the BNO085 sensor for additional functionality. The push button is used for user input.
Component List
Seeeduino XIAO
Description: A compact microcontroller board based on the SAMD21G18 chip.
Pins: A0 - D0 - DAC, A1 - D1, A2 - D2, A3 - D3, A4 - D4 - SDA, A5 - D5 - SCL, A6 - D6 - TX, 5V, GND, 3V3, A10 - D10 - MOSI, A9 - D9 - MISO, A8 - D8 - SCK, A7 - D7 - RX
ULN2803 Darlington Array
Description: A high-voltage, high-current Darlington transistor array.
Pins: I1, I2, I3, I4, I5, I6, I7, I8, O1, O2, O3, O4, O5, O6, O7, O8, GND, COMMON
COIN VIBRATION MOTOR
Description: A small, compact motor used for haptic feedback.
Pins: +, -
BNO085
Description: A 9-axis sensor providing orientation and motion data.
Pins: VCC, GND, SCL/SCK/RX, SDA/MISO/TX, ADR/MOSI, CS, INT, RST, PS1, PS0
MCP23S17
Description: A 16-bit I/O expander with SPI interface.
Pins: GPB0, GPB1, GPB2, GPB3, GPB4, GPB5, GPB6, GPB7, A1, A0, SO, SI, CS, VSS, VDD, INTA, INTB, RESET, A2, GPA1, GPA0, GPA5, GPA4, GPA3, GPA2, GPA7, GPA6, SCK
Push Button
Description: A simple push button for user input.
Pins: pin1, pin2
Wiring Details
Seeeduino XIAO
- A7 - D7 - RX is connected to CS of MCP23S17.
- A8 - D8 - SCK is connected to SCK of MCP23S17.
- A10 - D10 - MOSI is connected to SI of MCP23S17.
- A9 - D9 - MISO is connected to SO of MCP23S17.
- A5 - D5 - SCL is connected to SCL/SCK/RX of BNO085.
- A4 - D4 - SDA is connected to SDA/MISO/TX of BNO085.
- A6 - D6 - TX is connected to pin2 of the push button.
- 3V3 is connected to VCC of BNO085 and VDD of MCP23S17.
- GND is connected to GND of BNO085, pin1 of the push button, GND of both ULN2803 Darlington Arrays, and VSS of MCP23S17.
ULN2803 Darlington Array (1)
- I1 is connected to GPA7 of MCP23S17.
- I2 is connected to GPA6 of MCP23S17.
- I3 is connected to GPA5 of MCP23S17.
- I4 is connected to GPA4 of MCP23S17.
- I5 is connected to GPA3 of MCP23S17.
- I6 is connected to GPA2 of MCP23S17.
- I7 is connected to GPA1 of MCP23S17.
- I8 is connected to GPA0 of MCP23S17.
- COMMON is connected to the positive terminals of multiple coin vibration motors.
ULN2803 Darlington Array (2)
- I1 is connected to GPB7 of MCP23S17.
- I2 is connected to GPB6 of MCP23S17.
- I3 is connected to GPB5 of MCP23S17.
- I4 is connected to GPB4 of MCP23S17.
- I5 is connected to GPB3 of MCP23S17.
- I6 is connected to GPB2 of MCP23S17.
- I7 is connected to GPB1 of MCP23S17.
- I8 is connected to GPB0 of MCP23S17.
- COMMON is connected to the positive terminals of multiple coin vibration motors.
COIN VIBRATION MOTORS
The negative terminals of the motors are connected to the outputs of the ULN2803 Darlington Arrays.
BNO085
- GND is connected to the common ground.
- VCC is connected to the 3.3V supply.
- SCL/SCK/RX and SDA/MISO/TX are connected to the corresponding pins on the Seeeduino XIAO.
MCP23S17
- CS, SCK, SI, and SO are connected to the corresponding pins on the Seeeduino XIAO.
- VDD is connected to the 3.3V supply.
- VSS is connected to the common ground.
Push Button
- pin1 is connected to the common ground.
- pin2 is connected to A6 - D6 - TX of the Seeeduino XIAO.