Circuit Documentation
Summary
This circuit is a complex system that integrates a Seeeduino XIAO microcontroller, an MCP23S17 I/O expander, two ULN2803 Darlington Arrays, multiple coin vibration motors, a BNO085 sensor, a TPS63031 power management IC, and other components such as resistors, potentiometers, and push buttons. The circuit is designed to control multiple outputs, including vibration motors, and interfaces with sensors and other peripherals through I2C and SPI communication protocols. The power supply is managed by a TPS63031, which regulates the voltage from 18650 batteries.
Component List
Seeeduino XIAO
Description: A compact microcontroller board based on the SAMD21G18 chip.
Pins: A0 - D0 - DAC, A1 - D1, A2 - D2, A3 - D3, A4 - D4 - SDA, A5 - D5 - SCL, A6 - D6 - TX, 5V, GND, 3V3, A10 - D10 - MOSI, A9 - D9 - MISO, A8 - D8 - SCK, A7 - D7 - RX
MCP23S17
Description: 16-bit I/O expander with SPI interface.
Pins: GPB0, GPB1, GPB2, GPB3, GPB4, GPB5, GPB6, GPB7, A1, A0, SO, SI, CS, VSS, VDD, INTA, INTB, RESET, A2, GPA1, GPA0, GPA5, GPA4, GPA3, GPA2, GPA7, GPA6, SCK
ULN2803 Darlington Array (2 units)
Description: High-voltage, high-current Darlington transistor array.
Pins: I1, I2, I3, I4, I5, I6, I7, I8, O3, O4, O5, O6, O7, O8, GND, COMMON, O1, O2
COIN VIBRATION MOTOR (6 units)
Description: Small DC motor that vibrates when powered.
Pins: +, -
TPS63031
Description: High-efficiency, single-inductor buck-boost converter.
Pins: VIN, NC, GND, OUT
18650 Battery (2 units)
Description: Rechargeable lithium-ion battery.
Pins: +, -
BNO085
Description: 9-axis absolute orientation sensor.
Pins: VCC, GND, SCL/SCK/RX, SDA/MISO/TX, ADR/MOSI, CS, INT, RST, PS1, PS0
Push Button
Description: Simple mechanical switch.
Pins: pin1, pin2
Resistor
Description: 10k Ohm resistor.
Pins: pin1, pin2
Properties: Resistance = 10,000 Ohms
Potentiometer Piher 10mm
Description: Variable resistor.
Pins: A, Variable, B
Comment V2
Description: Placeholder for comments or notes in the circuit.
Pins: None
Wiring Details
Seeeduino XIAO
3V3 is connected to:
BNO085 VCC
BNO085 ADR/MOSI
Push Button pin1
Potentiometer Piher 10mm B
TPS63031 OUT
MCP23S17 VDD
GND is connected to:
BNO085 GND
Resistor pin1
18650 Battery (-)
ULN2803 Darlington Array GND (both units)
Potentiometer Piher 10mm A
TPS63031 GND
MCP23S17 VSS, A2, A1, A0
- A0 - D0 - DAC is connected to MCP23S17 CS
- A8 - D8 - SCK is connected to MCP23S17 SCK
- A10 - D10 - MOSI is connected to MCP23S17 SI
- A9 - D9 - MISO is connected to MCP23S17 SO
- A3 - D3 is connected to:
Resistor pin2
Push Button pin2
- A2 - D2 is connected to Potentiometer Piher 10mm Variable
- A5 - D5 - SCL is connected to BNO085 SCL/SCK/RX
- A4 - D4 - SDA is connected to BNO085 SDA/MISO/TX
MCP23S17
- GPA7 is connected to ULN2803 Darlington Array I1 (first unit)
- GPA6 is connected to ULN2803 Darlington Array I2 (first unit)
- GPA5 is connected to ULN2803 Darlington Array I3 (first unit)
- GPA4 is connected to ULN2803 Darlington Array I4 (first unit)
- GPA3 is connected to ULN2803 Darlington Array I5 (first unit)
- GPA2 is connected to ULN2803 Darlington Array I6 (first unit)
- GPA1 is connected to ULN2803 Darlington Array I7 (first unit)
- GPA0 is connected to ULN2803 Darlington Array I8 (first unit)
- GPB7 is connected to ULN2803 Darlington Array I1 (second unit)
- GPB6 is connected to ULN2803 Darlington Array I2 (second unit)
- GPB5 is connected to ULN2803 Darlington Array I3 (second unit)
- GPB4 is connected to ULN2803 Darlington Array I4 (second unit)
- GPB3 is connected to ULN2803 Darlington Array I5 (second unit)
- GPB2 is connected to ULN2803 Darlington Array I6 (second unit)
- GPB1 is connected to ULN2803 Darlington Array I7 (second unit)
- GPB0 is connected to ULN2803 Darlington Array I8 (second unit)
ULN2803 Darlington Array (First Unit)
- O8 is connected to COIN VIBRATION MOTOR (-)
- O7 is connected to COIN VIBRATION MOTOR
- O6 is connected to COIN VIBRATION MOTOR
ULN2803 Darlington Array (Second Unit)
- O1 is connected to COIN VIBRATION MOTOR
- O2 is connected to COIN VIBRATION MOTOR
- O3 is connected to COIN VIBRATION MOTOR TPS63031
VIN is connected to:
18650 Battery (+)
COIN VIBRATION MOTOR (+) (all instances)
ULN2803 Darlington Array COMMON (both units)
18650 Battery
- is connected to:
18650 Battery Documented Code
There is no embedded code provided for this circuit. The microcontroller and other programmable components are expected to be programmed externally to achieve the desired functionality.