Circuit Documentation
Summary
This circuit is a complex embedded system that integrates a variety of components, including a microcontroller, a port expander, a Darlington array, vibration motors, a power management IC, a battery, a sensor, a push button, and a potentiometer. The circuit is designed to control multiple vibration motors using a microcontroller and a port expander, with power supplied by a battery and regulated by a power management IC. The system also includes a sensor for additional functionality and a potentiometer for user input.
Component List
Seeeduino XIAO
Description: A compact microcontroller board based on the SAMD21 microcontroller.
Pins: A0 - D0 - DAC, A1 - D1, A2 - D2, A3 - D3, A4 - D4 - SDA, A5 - D5 - SCL, A6 - D6 - TX, 5V, GND, 3V3, A10 - D10 - MOSI, A9 - D9 - MISO, A8 - D8 - SCK, A7 - D7 - RX
MCP23S17
Description: A 16-bit I/O expander with SPI interface.
Pins: GPB0, GPB1, GPB2, GPB3, GPB4, GPB5, GPB6, GPB7, A1, A0, SO, SI, CS, VSS, VDD, INTA, INTB, RESET, A2, GPA1, GPA0, GPA5, GPA4, GPA3, GPA2, GPA7, GPA6, SCK
ULN2803 Darlington Array (2 units)
Description: A high-voltage, high-current Darlington transistor array.
Pins: I1, I2, I3, I4, I5, I6, I7, I8, O3, O4, O5, O6, O7, O8, GND, COMMON, O1, O2
COIN VIBRATION MOTOR (7 units)
Description: A small motor that provides vibration feedback.
Pins: +, -
TPS63031
Description: A high-efficiency, low-power buck-boost converter.
Pins: VIN, NC, GND, OUT
18650 Battery (2 units)
Description: A rechargeable lithium-ion battery.
Pins: +, -
BNO085
Description: A 9-axis sensor with accelerometer, gyroscope, and magnetometer.
Pins: VCC, GND, SCL/SCK/RX, SDA/MISO/TX, ADR/MOSI, CS, INT, RST, PS1, PS0
Push Button
Description: A simple push button for user input.
Pins: pin1, pin2
Potentiometer Piher 10mm
Description: A variable resistor for adjusting resistance.
Pins: A, Variable, B
Wiring Details
Seeeduino XIAO
- A0 - D0 - DAC: Connected to MCP23S17 CS
- A8 - D8 - SCK: Connected to MCP23S17 SCK
- A10 - D10 - MOSI: Connected to MCP23S17 SI
- A9 - D9 - MISO: Connected to MCP23S17 SO
- A6 - D6 - TX: Connected to Push Button pin2
- A3 - D3: Connected to Potentiometer Piher 10mm Variable
- A5 - D5 - SCL: Connected to BNO085 SCL/SCK/RX
- A4 - D4 - SDA: Connected to BNO085 SDA/MISO/TX
- A7 - D7 - RX: Connected to MCP23S17 VDD
- 3V3: Connected to BNO085 VCC, ADR/MOSI, Potentiometer Piher 10mm B, TPS63031 OUT
- GND: Connected to BNO085 GND, Push Button pin1, 18650 -, ULN2803 Darlington Array GND, Potentiometer Piher 10mm A, TPS63031 GND, MCP23S17 VSS, A2, A1, A0
MCP23S17
- GPA7: Connected to ULN2803 Darlington Array I1
- GPA6: Connected to ULN2803 Darlington Array I2
- GPA5: Connected to ULN2803 Darlington Array I3
- GPA4: Connected to ULN2803 Darlington Array I4
- GPA3: Connected to ULN2803 Darlington Array I5
- GPA2: Connected to ULN2803 Darlington Array I6
- GPA1: Connected to ULN2803 Darlington Array I7
- GPA0: Connected to ULN2803 Darlington Array I8
- GPB7: Connected to ULN2803 Darlington Array I1 (second unit)
- GPB6: Connected to ULN2803 Darlington Array I2 (second unit)
- GPB5: Connected to ULN2803 Darlington Array I3 (second unit)
- GPB4: Connected to ULN2803 Darlington Array I4 (second unit)
- GPB3: Connected to ULN2803 Darlington Array I5 (second unit)
- GPB2: Connected to ULN2803 Darlington Array I6 (second unit)
- GPB1: Connected to ULN2803 Darlington Array I7 (second unit)
- GPB0: Connected to ULN2803 Darlington Array I8 (second unit)
ULN2803 Darlington Array
- O1: Connected to COIN VIBRATION MOTOR - (first unit)
- O2: Connected to COIN VIBRATION MOTOR - (second unit)
- O3: Connected to COIN VIBRATION MOTOR - (third unit)
- O8: Connected to COIN VIBRATION MOTOR - (fourth unit)
- O7: Connected to COIN VIBRATION MOTOR - (fifth unit)
- O6: Connected to COIN VIBRATION MOTOR - (sixth unit)
COIN VIBRATION MOTOR
- +: Connected to 18650 + (first unit)
- +: Connected to 18650 + (second unit)
- +: Connected to 18650 + (third unit)
- +: Connected to 18650 + (fourth unit)
- +: Connected to 18650 + (fifth unit)
- +: Connected to 18650 + (sixth unit)
- +: Connected to 18650 + (seventh unit)
TPS63031
- VIN: Connected to 18650 +
- OUT: Connected to Seeeduino XIAO 3V3
18650 Battery
- -: Connected to GND net
- +: Connected to COIN VIBRATION MOTOR +, TPS63031 VIN
BNO085
- VCC: Connected to Seeeduino XIAO 3V3
- GND: Connected to GND net
- SCL/SCK/RX: Connected to Seeeduino XIAO A5 - D5 - SCL
- SDA/MISO/TX: Connected to Seeeduino XIAO A4 - D4 - SDA
Push Button
- pin1: Connected to GND net
- pin2: Connected to Seeeduino XIAO A6 - D6 - TX
Potentiometer Piher 10mm
- A: Connected to GND net
- Variable: Connected to Seeeduino XIAO A3 - D3
- B: Connected to Seeeduino XIAO 3V3
Code Documentation
There is no embedded code provided for this circuit. The microcontroller and other programmable components are not configured with any specific code in this documentation.